4.1b Further Mechanics
Circular Motion

| Lessons | Topics |
| --- | --- |
| 1 to 3 | Circular motion Motion in a circular path at constant speed implies there is an acceleration and requires a centripetal force. Angular speed ω = v / r = 2π f Centripetal acceleration a = v2 / r = ω2 r Centripetal force F = mv2 / r = mω2 r The derivation of a = v2/ r will not be examined. |

Uniform Circular Motion

Consider an object moving around a circular path of radius, r  with a constant linear speed , v

The circumference of this circle is 2π r.

The time taken to complete one circle, the period, is T.

Therefore:

v = 2π r / T

But frequency, f = 1 / T and so also:

v = 2π r f

Note: The arrows represent the velocity of the object. As the direction is continually changing, so is the velocity.

Q. The tyre of a car, radius 40cm, rotates with a frequency of 20 Hz. Calculate (a) the period of rotation and (b) the linear speed at the tyres edge.

(a)

(b)

Angular displacement, θ

Angular displacement, θ is equal to the angle swept out at the centre of the circular path.

An object completing a complete circle will therefore undergo an angular displacement of 360°.

½ circle = 180°.

¼ circle = 90°.

Angles in radians

The radian (rad) is defined as the angle swept out at the centre of a circle when the arc length, s is equal to the radius, r of the circle.

If s = r

then θ = 1 radian

The circumference of a circle = 2πr

Therefore 1 radian = 360° / 2π = 57.3°

And so:

360° = 2π radian  (6.28 rad)

180° = π radian     (3.14 rad)

90° = π / 2 radian  (1.57 rad)

Also:  s = r θ

Angular speed (ω)

ω  =  Δθ  /  Δt

units:

angular displacement (θ ) in radians (rad)

time (t ) in seconds (s)

angular speed (ω) in radians per second (rad s-1)

Angular speed can also be measured in revolutions per second (rev s-1) or revolutions per minute (r.p.m.)

Q. Calculate the angular speed in rad s-1 of an old vinyl record player set at 78 r.p.m.

Angular frequency (ω)

Angular frequency is the same as angular speed.

For an object taking time, T to complete one circle of angular displacement 2π:

ω = 2π / T

but T = 1 / f

therefore:   			ω = 2π f

that is: angular frequency = 2π x frequency

Relationship between angular and linear speed

For an object taking time period, T to complete a circle radius r:

ω = 2π / T

rearranging: T = 2π / ω

but: v = 2π r  / T

= 2π r  / (2π / ω)

Therefore:

v = r ω

and:

ω  =  v / r

Q. A hard disc drive, radius 50.0 mm, spins at 7200 r.p.m. Calculate (a) its angular speed in rad s-1; (b) its outer edge linear speed.

| angular speed | linear speed | radius |
| --- | --- | --- |
|  | 6 ms-1 | 0.20 m |
| 40 rad s-1 |  | 0.50 m |
| 6 rad s-1 | 18 ms-1 |  |
|  | 48 cms-1 | 4.0 m |
| 45 r.p.m. |  | 8.7 cm |

Centripetal acceleration (a)

An object moving along a circular path is continually changing in direction. This means that even if it is travelling at a constant speed, v it is also continually changing its velocity. It is therefore undergoing an acceleration, a.

This acceleration is directed towards the centre (centripetal) of the circular path and is given by:

but: v = r ω

combining this with:

gives:

and also:

| angular speed | linear speed | radius | centripetal acceleration |
| --- | --- | --- | --- |
|  | 8.0 ms-1 | 2.0 m |  |
| 2.0 rad s-1 |  | 0.50 m |  |
| 9.0 rad s-1 | 27 ms-1 |  |  |
|  | 6.0 ms-1 |  | 9.0 ms-2 |
| 33⅓ r.p.m. |  |  | 1.8 ms-2 |

ISS Question

For the International Space Station in orbit about the Earth (ISS)

Calculate:

(a) the centripetal acceleration and

(b) linear speed

Data:

orbital period = 90 minutes

orbital height = 400km

Earth radius = 6400km

Centripetal Force

Newton’s first law:

If a body is accelerating it must be subject to a resultant force.

Newton’s second law:

The direction of the resultant force and the acceleration must be the same.

Therefore centripetal acceleration requires a resultant force directed towards the centre of the circular path – this is CENTRIPETAL FORCE.

What happens when centripetal force is removed?

When the centripetal force is removed the object will move along a straight line tangentially to the circular path.

Other examples of centripetal forces

| Situation | Centripetal force |
| --- | --- |
| Earth orbiting the Sun | GRAVITY of the Sun |
| Car going around a bend. | FRICTION on the car’s tyres |
| Airplane banking (turning) | PUSH of air on the airplane’s wings |
| Electron orbiting a nucleus | ELECTROSTATIC attraction due to opposite charges |

Equations for centripetal force

From Newton’s 2nd law of motion:

ΣF = ma

If a = centripetal acceleration

then ΣF = centripetal force

and so:

ΣF = m v2 / r

and 	ΣF = m r ω2

and 	ΣF = m v ω

Q1. Calculate the centripetal tension force in a string used to whirl a mass of 200g around a horizontal circle of radius 70cm at 4.0ms-1.

Q2.Calculate the maximum speed that a car of mass 800kg can go around a curve of radius 40m if the maximum frictional force available is 8kN.

Q3. A mass of 300g is whirled around a vertical circle using a piece of string of length 20cm at 3.0 revolutions per second.

Calculate the tension in the string at positions:

(a) A – top

(b) B – bottom and

(c) C – string horizontal

(a) A – top

(b) B – bottom

(c) C – horizontal string

# Text boxes

r

v

r

v

r

v

r

v

r

v

θ

meow!

s

r

r

θ

Question 4

A

B

C

Forces on Jess

R

Calculate the maximum speed that Pat can drive over the bridge for Jess to stay in contact with the van’s roof if the distance that Jess is from the centre of curvature is 8.0m.

mg