4.4 Fields 
Capacitance

Breithaupt pages 94 to 101

| Lessons | Topics |
| --- | --- |
| 1 | Capacitance Definition of capacitance; C = Q / V |
| 2 | Energy stored by a capacitor Derivation of E = ½ Q V and interpretation of area under a graph of charge against p.d. E = ½ Q V = ½ C V2 = ½ Q2/ C |
| 3 to 5 | Capacitor discharge Graphical representation of charging and discharging of capacitors through resistors, Time constant = RC, Calculation of time constants including their determination from graphical data, Quantitative treatment of capacitor discharge, Q = Qo e- t/RC Candidates should have experience of the use of a voltage sensor and datalogger to plot discharge curves for a capacitor. |

Capacitors

A capacitor is a device for storing electrical charge.

Most capacitors consist of two parallel conductors (plates) separated by a thin insulator (air in the simplest case), or dielectric.

Uses of capacitors include:

- voltage regulation in power supplies,

- timing circuits,

- tuning circuits

- in back-up power supplies.

http://electronics.howstuffworks.com/capacitor.htm

MAKE presents: The Capacitor http://www.youtube.com/watch?v=ZYH9dGl4gUE

Capacitor charging

When a voltage is connected to the capacitor electrons flow off one of the plates (which becomes positive) and onto the other (which becomes negative)

The rate of flow of charge (electric current) falls exponentially in time from an initial value, Io as the capacitor becomes fully charged. This is because it becomes more and more difficult to remove electrons from the positive plate.

The charging of a capacitor is analogous to the inflating of a tyre with a pump:

tyre size = capacitance

pump pressure = applied voltage

air flow rate = charge flow rate, current

Capacitance (C)

The capacitance of a capacitor is defined as the charge stored per unit potential difference change

unit of capacitance: farad (F)

also: Q = CV    and   V = Q / C

Question

A capacitor of 500μF is charged by a power supply 4V through a 200Ω resistor. Calculate (a) the initial charging current and (b) the final charge stored on the capacitor.

(a) Initially the capacitor voltage is zero and all 4V of the power supply will be across the resistor.

(b) At the end of the charging process, all 4V will be across the capacitor.

| charge | potential difference | capacitance |
| --- | --- | --- |
| 300 μC | 6 V |  |
|  | 5 V | 40 μF |
| 720 μC |  | 60 μF |
| 500 nC |  | 20 nF |
| 2 μC | 40 mV |  |
|  | 9 V | 100 pF |

Energy stored by a capacitor

Consider a capacitor of capacitance C with charge q.

To add a further small amount of charge Δq requires work ΔW where

v = average potential difference during the process.

The work ΔW is represented by the green area on the graph.

The total work W done in charging the capacitor by charge Q to potential difference V is equal to the area under the curve.

= ½ x base x height

W = ½ QV

This is also the energy stored by the capacitor

Energy equations

W = ½ QV

substituting Q = C V gives:

substituting V = Q / C gives:

Question

Calculate the energy stored when:

(a) a 10μF capacitor is charged by 12V

(b) 200μC is placed on a capacitor using 6V

(c) a 0.05μF capacitor receives 40 nC of charge.

Capacitor Discharge

A capacitor C is discharged through a resistor R.

The charge Q left on a capacitor, initially charged to Qo after time t is given by:

Q = Qo e – t / RC

Also:

and:

Time Constant (RC)

This is the time taken for the capacitor to discharge to 0.37 of its initial charge.

It is also the time taken for the discharge current and potential difference to fall to 0.37 of their initial values.

Why RC is called the time constant

time constant = RC

Substituting R = V / I  and  C = Q / V gives:

time constant = (V x Q) / (I x V)

= Q / I

but Q = I x t

time constant = I x t / I

= t

Why 0.37 ?

Q = Qo e – t / RC

When the time t = RC

Q = Qo e – 1

Q / Qo = e – 1

Q / Qo = 0.3679

Which is approximately 0.37

Questions

1. Calculate the time taken for a capacitor of 1500 μF to discharge to 0.37 of its initial charge through a resistance of 2 kΩ.

2. A capacitor of 5000 μF is charged by a 12 V supply and then discharged through a 150 Ω resistor.

Calculate (a) its initial charge,

(b) the time constant

(c) the charge remaining after 1.5 seconds.